Sub-class 14

| Parameter | Description | Comments |
| --- | --- | --- |
| Frequency band | 1 610 - 1 613.5 MHz 1 613.8 - 1 626.5 MHz 2 483.5 - 2 500 MHz | transmit (Earth-to-space) receive (space-to-Earth) receive (space-to-Earth) |
| Radio service according ITU Radio Regulation | Land Mobile-Satellite Service |  |
| Application | "Satellite-Personal Communications earth stations" applications. |  |
| Channel Spacing | to be defined by the satellite operator |  |
| RF – Power | not defined |  |
| Emission density e.i.r.p. | -3 dB (W/4 kHz), (mean limit) -15 dB (W/4 kHz), (peak limit) | In this context, the mean is the mean over time whilst the MES is in the carrier-on mode |
| Transmit / Receive spacing (Duplex direction) | to be defined by the satellite operator |  |
| Type(s) of modulation | to be defined by the satellite operator |  |
| Transmission capacity | to be defined by the satellite operator |  |
| Harmonised Standard representing the state of art | EN 301 441 |  |
| Equipment class according to Commission Decision 2000/299/EC | Class 1 |  |