Last updated March 2007

Sub-class 19

| Parameter | Description | Comments |
| --- | --- | --- |
| Frequency band | 40.660-40.700 MHz |  |
| Radio service according ITU Radio Regulation | Mobile Service |  |
| Application | Non-Specific Short Range Devices (Video applications are excluded) | This category is available for any type of application which fulfils the technical conditions (typical uses are telemetry, telecommand, alarms, data in general and other similar applications). |
| Channel Spacing |  |  |
| RF – Power | not defined |  |
| RF – Radiated Power | 10 mW e.r,p. |  |
| Transmit / Receive spacing (Duplex direction) | not defined |  |
| Type(s) of modulation | not defined |  |
| Duty cycle | Not restricted |  |
| Harmonised Standard representing the state of art | EN 300 220 - 2 |  |
| Equipment class according to Commission Decision 2000/299/EC* | Class 1 |  |