Sub-class 19

| Parameter | Description | Comments |
| --- | --- | --- |
| Frequency band | 40.665 MHz, 40.675 MHz, 40.685 MHz, 40.695 MHz |  |
| Radio service according ITU Radio Regulation | Mobile Service |  |
| Application | Non-Specific Short Range Devices | Telemetry, Telecommand, Alarms, Data in general and other similar applications. Video applications are excluded |
| Channel Spacing |  |  |
| RF – Power | not defined |  |
| RF – Radiated Power | 10 mW e.r,p. |  |
| Transmit / Receive spacing (Duplex direction) | not defined |  |
| Type(s) of modulation | not defined | Applications employing audio and voice signals are excluded |
| Duty cycle | ≤ 100 % |  |
| Harmonised Standard representing the state of art | EN 300 220 - 3 |  |
| Equipment class according to Commission Decision 2000/299/EC* | Class 1 |  |