Sub-class 9

| Parameter | Description | Comments |
| --- | --- | --- |
| Frequency band | 1 710 - 1 785 MHz 1 805 - 1 880 MHz | (transmit) (receive) |
| Radio service according ITU Radio Regulation | MOBILE Service |  |
| Application | GSM | end user terminals |
| Channel Spacing | 200 kHz |  |
| RF – Power | 1 W (30dBm) 0.25 W (24 dBm) 4 W (36 dBm) | Power class 1 Power class 2 Power class 3 |
| RF – Radiated Power | not defined |  |
| Transmit / Receive spacing (Duplex direction) | 95 MHz |  |
| Type(s) of modulation | 200KG7WDT Gaussian Minimum Shift Keying (GMSK) |  |
| Transmission Capacity / Duty cycle/ Channel access protocol | not defined |  |
| Harmonised Standard representing the state of art | EN 301 419-1 EN 301 419-2 EN 301 419-3 EN 301 419-7 |  |
| Equipment class according to Commission Decision 2000/299/EC | Class 1 |  |