Classification of radio equipment - Commission Decision 2000/299/EC (6.4.2000)

Sub-class 18 Rev. 1

| Parameter | Description | Comments |
| --- | --- | --- |
| Frequency band | 1880 MHz – 1900 MHz |  |
| Radio service according ITU Radio Regulation | Mobile Service |  |
| Application | DECT | user terminals equipment |
| Channel Spacing | 1728 kHz |  |
| RF – Power | not defined |  |
| RF – Radiated Power | 250 mWatt peak e.r.p. (peak power over time-slot) | Type of Antenna: integral or dedicated |
| Transmit / Receive spacing (Duplex direction) | See EN 301 406 | TDD |
| Type(s) of modulation | See EN 301 406 |  |
| Transmission capacity | See EN 301 406 |  |
| Harmonised Standard representing the state of art | EN 301 406 |  |
| Equipment class according to Commission Decision 2000/299/EC* | Class 1 |  |