Sub-class 12

| Parameter | Description | Comments |
| --- | --- | --- |
| Frequency band | 10.70 GHz - 11.70 GHz 12.50 GHz - 12.75 GHz 14.00 GHz - 14.25 GHz | (space-to-Earth) (space-to-Earth) (Earth to space) |
| Radio service according ITU Radio Regulation | Land Mobile-Satellite Service |  |
| Application | Land Mobile Earth Stations applications |  |
| Channel Spacing | to be defined by the satellite operator |  |
| RF – Power | to be defined by the satellite operator |  |
| Emission density e.i.r.p. | 33 - 25 log (φ + δφ) - 10 log (K) dBW/40 kHz where 2,5° ≤φ+ δφ ≤7,0°; +12 - 10 log (K) dBW/40 kHz where 7,0° <φ + δφ ≤9,2°; 36 - 25 log (φ + δφ ) - 10 log (K) dBW/40 kHz where 9,2° <φ + δφ ≤48°; -6 - 10 log (K) dBW/40 kHz where 48° <φ + δφ ≤180° | φ is the angle, in degrees, between the main beam axis and the direction considered. K is the power density ratio between the fully loaded system and a single LMES measured in a 40 kHz bandwidth |
| Transmit / Receive spacing (Duplex direction) | to be defined by the satellite operator |  |
| Type(s) of modulation | to be defined by the satellite operator |  |
| Transmission capacity | to be defined by the satellite operator |  |
| Harmonised Standard representing the state of art | EN 301 427 |  |
| Equipment class according to Commission Decision 2000/299/EC* | Class 1 |  |